## Slide 1: STM32F103C8T6 Microcontroller
Device: STM32F103C8T6 Family: STM32F1 Core: ARM Cortex-M3
Presented by: Eyoel Issayas
Low-Power Architecture and Modes

## Slide 2: Introduction
The STM32F103C8T6 is a 32-bit microcontroller manufactured by STMicroelectronics.
Main features:
ARM Cortex-M3 processor
Maximum frequency: 72 MHz
64 KB Flash
20 KB SRAM
2 × 12-bit ADC
Timers
USART, SPI and I²C
USB and CAN
GPIO and external interrupts
Low-power modes
It operates from a 2.0–3.6 V supply.

## Slide 3: STM32 Architecture
The main parts of the STM32F103C8T6 are:
Cortex-M3 CPU – executes instructions
Flash memory – stores the program
SRAM – stores temporary data
RCC – controls clocks
GPIO – controls input/output pins
NVIC – manages interrupts
EXTI – handles external interrupt/event lines
PWR – controls power and low-power modes
Peripherals – timers, ADC, USART, SPI, I²C, etc.
The peripherals are connected through the STM32's internal AHB and APB buses.

## Slide 4: Cortex-M3 Core
The STM32F103C8T6 uses an ARM Cortex-M3 processor.
Important features:
32-bit processor
Maximum frequency of 72 MHz
Hardware multiplication and division
NVIC interrupt controller
Supports WFI
Supports WFE
The Cortex-M3 can stop its CPU clock when the processor has no work to do.
This helps reduce power consumption.

## Slide 5: Clock System
The RCC (Reset and Clock Control) manages the microcontroller's clock system.
The STM32F103C8T6 has:
External high-speed oscillator: 4–16 MHz
Internal high-speed RC: 8 MHz
Internal low-speed RC: about 40 kHz
External 32.768 kHz oscillator for RTC
PLL for generating the CPU clock
The CPU can operate at up to 72 MHz.
Low-power principle:
Unused clock → Disable it → Reduce power consumption

## Slide 6: GPIO
GPIO = General-Purpose Input/Output
GPIO pins can be used as:
Digital inputs
Digital outputs
Alternate functions
Analog inputs
GPIO can also be connected to the EXTI controller.
For example:
Button → GPIO → EXTI → Interrupt → CPU wakes
The STM32F103 family supports external interrupt functionality through its GPIO system.

## Slide 7: Interrupt Controller
The NVIC (Nested Vectored Interrupt Controller) is part of the Cortex-M3.
- It:
Enables and disables interrupts
Handles interrupt priorities
Detects interrupt requests
Sends the CPU to an interrupt handler
Interrupts are important for low-power operation.
Instead of continuously checking a button:
Sleep → Button pressed → Interrupt → Wake up
This saves energy.

## Slide 8: Peripheral Architecture
The STM32F103C8T6 contains many peripherals.
Examples:
GPIO
Timers
ADC
USART
SPI
I²C
USB
CAN
RTC
DMA
These peripherals communicate with the CPU through the internal bus architecture.
The RCC can also control the clocks supplied to peripherals.
Therefore:
Peripheral not needed → Clock disabled → Less power

## Slide 9: STM32F103 Low-Power Modes
The STM32F103 has three main low-power modes:
Sleep
Stop
Standby
Important:
The STM32F103C8T6 does not have separate Low-power Sleep or Shutdown modes like some newer STM32 families.
ST's RM0008 reference manual explicitly lists Sleep, Stop and Standby as the STM32F10xxx low-power modes.

## Slide 10: Sleep Mode
Sleep Mode
In Sleep mode:
CPU clock is stopped
Peripherals remain running
NVIC remains active
Memory is retained
Power consumption is reduced
The MCU can wake when an interrupt occurs.
Example:
CPU working → WFI → Sleep → Timer interrupt → CPU wakes
Sleep is useful when the CPU needs to wait but peripherals still need to operate.
ST specifies that Sleep can be entered using WFI or WFE.

## Slide 11: Stop Mode
Stop Mode
Stop mode provides greater power savings than Sleep.
In Stop mode:
CPU stops
All clocks are stopped
HSI and HSE oscillators are stopped
SRAM contents are retained
Voltage regulator can remain on or enter low-power mode
The MCU can wake through configured EXTI lines.
Example:
Run → Stop → External interrupt → Wake → Run
Stop mode is useful for battery-powered applications.

## Slide 12: Standby Mode
Standby Mode
Standby provides the lowest power consumption of the three modes.
In Standby:
CPU is stopped
Most clocks are stopped
Voltage regulator is turned off
Main 1.8 V domain is powered down
Possible wake-up sources include:
WKUP pin
RTC alarm
External reset
Independent watchdog reset
Example:
Standby → Button pressed → Wake → MCU restarts

## Slide 13: Low-Power Mode Comparison
Feature | Sleep | Stop | Standby
CPU | Off | Off | Off
Clocks | Mostly running | Stopped | Stopped
SRAM | Retained | Retained | Not generally retained
Power saving | Low | High | Very high
Wake-up | Interrupt | EXTI | WKUP/RTC/reset/IWDG
Voltage regulator | On | On/Low-power | Off
Simple idea:
Sleep → Stop → Standby
As power consumption decreases, the MCU loses more functionality.
This comparison is based on ST's official RM0008 low-power-mode table.

## Slide 14: PWR Registers
The PWR (Power Control) peripheral controls low-power operation.
Important registers include:
PWR_CR
Power Control Register
Controls:
Low-power regulator
Power-down/standby selection
Voltage detector functions
Important bits include:
LPDS – Low-power deepsleep
PDDS – Power-down deepsleep selection
PWR_CSR
Power Control/Status Register
Contains:
Wake-up flag
Low-power regulator status
Other power-related status information
These registers are used when configuring Stop and Standby modes.

## Slide 15: RCC Registers
Important RCC registers include:
RCC_CR
Controls the main clock sources.
RCC_CFGR
Controls:
System clock selection
Prescalers
PLL configuration
RCC_APB1ENR
Enables clocks for APB1 peripherals.
RCC_APB2ENR
Enables clocks for APB2 peripherals.
RCC_AHBENR
Enables clocks for AHB peripherals.
Clock gating is important for reducing power consumption because unused peripheral clocks can be disabled.

## Slide 16: Cortex-M3 SCR Register
The Cortex-M3 contains a System Control Register (SCR).
Important bits:
SLEEPDEEP
Determines whether the processor enters:
Normal Sleep
Deep Sleep
Stop and Standby use the deep-sleep mechanism.
SLEEPONEXIT
Allows the processor to automatically enter Sleep after finishing an interrupt service routine.
SEVONPEND
Controls whether pending interrupts can generate events.
Therefore:
SCR + PWR registers + WFI/WFE → Low-power mode

## Slide 17: EXTI Registers
EXTI = External Interrupt/Event Controller
Important registers include:
EXTI_IMR – Interrupt Mask Register
EXTI_EMR – Event Mask Register
EXTI_RTSR – Rising Trigger Selection
EXTI_FTSR – Falling Trigger Selection
EXTI_PR – Pending Register
For example:
Button pressed
↓
GPIO detects signal
↓
EXTI detects rising/falling edge
↓
NVIC receives interrupt
↓
CPU wakes
The reference manual specifies EXTI lines as wake-up sources for Stop mode.

## Slide 18: NVIC Registers
The NVIC controls interrupts.
Important registers include:
ISER – Interrupt Set-Enable Register
ICER – Interrupt Clear-Enable Register
ISPR – Interrupt Set-Pending Register
ICPR – Interrupt Clear-Pending Register
IPR – Interrupt Priority Register
These registers allow the programmer to configure which interrupts can wake or control the processor.

## Slide 19: Wake-Up Sources
The STM32F103C8T6 supports different wake-up sources depending on the low-power mode.
Sleep
Can wake through:
Interrupts
Events
Stop
Can wake through:
EXTI lines
External signals configured through EXTI
Standby
Can wake through:
WKUP pin
RTC alarm
NRST external reset
Independent watchdog reset

## Slide 20: GPIO Wake-Up Example
Imagine a battery-powered device with a button.
Normal operation
MCU is running
↓
No activity
Enter Stop mode
↓
Button pressed
GPIO detects signal
↓
EXTI generates interrupt
↓
NVIC handles interrupt
↓
MCU wakes
↓
Program continues
This allows the MCU to consume very little power while waiting for the user.

## Slide 21: RTC Wake-Up
The RTC (Real-Time Clock) can continue operating using the low-speed clock source.
It can be used to wake the MCU at a specific time.
Example:
Standby
↓
RTC alarm after 10 minutes
↓
MCU wakes
↓
Perform task
↓
Return to low-power mode
This is useful for devices that only need to perform a task periodically.

## Slide 22: WFI
WFI = Wait For Interrupt
WFI tells the processor to wait for an interrupt.
Basic operation:
Program running
↓
WFI
↓
CPU sleeps
↓
Interrupt occurs
↓
CPU wakes
WFI is commonly used when the system is waiting for an interrupt from a timer, GPIO, USART, or another peripheral.
ST specifies WFI as an entry mechanism for the STM32F103 low-power modes.

## Slide 23: WFE
WFE = Wait For Event
WFE tells the processor to wait for an event.
Basic operation:
Program running
↓
WFE
↓
CPU waits
↓
Event occurs
↓
CPU wakes
WFE is useful when the application is designed around events rather than directly waiting for an interrupt.
STM32F103 low-power modes can use either WFI or WFE, depending on the desired wake-up mechanism.

## Slide 24: WFI vs WFE
WFI | WFE
Wait For Interrupt | Wait For Event
Waits for an interrupt | Waits for an event
Common for interrupt-driven systems | Useful for event-driven systems
Interrupt wakes processor | Event wakes processor
Can lead to an interrupt handler | Event does not necessarily require an interrupt handler
Easy way to remember:
WFI → Interrupt
WFE → Event

## Slide 25: Complete Low-Power Process
A typical STM32 low-power system works like this:
1. MCU performs its task
↓
2. MCU has nothing to do
↓
3. Configure PWR/RCC/EXTI
↓
4. Set SLEEPDEEP if required
↓
5. Execute WFI or WFE
↓
6. MCU enters low-power mode
↓
7. Wake-up source occurs
↓
8. MCU wakes
↓
9. Program continues

## Slide 26: Real-World Application
Battery-Powered Temperature Sensor
The STM32 could work like this:
Read temperature
↓
Send data
↓
Enter Stop mode
↓
Wait for RTC/timer or external event
↓
Wake up
↓
Read temperature again
↓
Send data
↓
Return to Stop mode
This saves much more energy than keeping the CPU running continuously.

## Slide 27: Why Low-Power Architecture Is Important
Low-power operation is useful in:
Battery-powered devices
IoT devices
Sensors
Wearable devices
Remote monitoring systems
Portable electronics
The basic principle is:
Only use power when the microcontroller is actually doing something.
The STM32F103 achieves this through:
Clock control
Peripheral clock gating
Sleep
Stop
Standby
Interrupts
Events
RTC wake-up

## Slide 28: Conclusion
The STM32F103C8T6 uses an ARM Cortex-M3 architecture with several features that help reduce power consumption.
The three main low-power modes are:
Sleep → Stop → Standby
We also learned about:
RCC for clock management
PWR for power control
EXTI for external events
NVIC for interrupts
SCR for processor sleep control
WFI for waiting for interrupts
WFE for waiting for events
The main concept is:
When the CPU is not needed, put it to sleep and wake it only when necessary.

## Slide 29: References
STMicroelectronics – STM32F103C8 Product Page
STM32F103 Datasheet – DS5319
RM0008 – STM32F101xx/STM32F102xx/STM32F103xx/STM32F105xx/STM32F107xx Reference Manual
PM0056 – STM32F10xxx Cortex-M3 Programming Manual
THANK YOU!